## Slide 1: the GrowSmarter project 2015-2019
Low Energy Districts Replication Workshop Suceava
Cologne

## Slide 2: Low Energy Districts Cologne
Contents
Introduction
Cologne Low Energy Districts Overview
Low Energy Districts Solutions Cologne
Q + A

## Slide 3: Low Energy Districts Cologne

## Slide 4: Low Energy Districts Cologne
ICT
Mobility
Energy
12 smart solutions
Low energy districts
Smart building shell refurbishment
Smart building logistics
Smart energy-saving tenants
Smart local electricity management
Sustainable urban mobility
9. Sustainable delivery
10. Smart traffic management
11. Alternative fuel driven vehicles
12. Smart mobility solutions
Integrated Infrastructures
5. Smart street lighting
6. Waste heat recovery
7. Smart waste collection
8. Big data management

## Slide 5: Low Energy Districts Cologne
3.1 Smart Home
3.1 Green Air
4.1 VPP - Siedlungsmanagement

## Slide 6: Low Energy Districts Cologne
Goal: Energy reduction by 70 %
Use of renewable energies
Insulation
Photovoltaics
Heatpumps
Storage batteries
Efficient lighting
Behavioural change (Smart Home & Smart Plugs & GreenAir)
Virtual Power Plant (Siedlungsmanagement)
Implementation strategy

## Slide 7: Low Energy Districts Cologne
Project area
Mülheim
Stegerwaldsiedlung
3 phases in 3 yrs construction time
  16 apartment blocks
  ~ 33.500 m² living space
  > 700 residential units
  > 1.000 tenants

## Slide 8
Innovative smart home system with components such as intelligent heating thermostats, window and door contacts and smart plugs
Information events in March & May 2018; all tenants of the project area were invited. Topics: Mieterstrom-model and Smart Home system.
Low number of participants in the study despite door-to-door offers.
Low Energy Districts - SmartHome Cologne
Notes: We were surprised at the low number of participants. The whole offer has, inclusive of installation, a value of about 1000 €.
The systems will become the property of the tenants upon completion of the study. We contacted all tenants , our customers (about 80 %) even in person, and informed these about our offer and invited them to our information events.

## Slide 9
SmartHome system includes:
1x homee Brain Cube (Base station)
1x Z-Wave Cube radio protocol through which all devices can communicate with each other
5x Intelligent heating thermostats
5x Door- windowsensors
3x Smart Plugs
Low Energy Districts - SmartHome Cologne
Notes: Z-Wave is the radio protocol through which all devices can communicate with each other

## Slide 10
GreenAir offers a room-air-monitoring service with ventilation and heating recommendations
Sensors measure temperature and humidity (optional motion detection - security) & will be installed in the apartements.
Data transmission is carried out using innovative LoRaWAN technology.
The main advantages are:
Mold prevention
Better well-being
Lower heating costs
Low Energy Districts - GreenAir monitoring system
Cologne
Notes: If the humidity rises above a value of 60%, the tenant gets a push-message with a ventilation recommendation.
The tenant's behaviour can therefore be preventively influenced such that he/she has a better indoor climate, saves
heating costs and significantly reduces the risk of mould formation.
Planned for the future:
The landlord receives a dashboard, which allows him/her to monitor an overview of the conditions in the properties. In
the run-up, reasonable limits can be agreed with the landlord.

## Slide 11
If humidity rises above 60% : the tenant gets a push-message with a ventilation recommendation.
Influences behavior:
Managing better indoor climate
saving heating costs and
significantly reducing the risk of mold formation.
Low Energy Districts - GreenAir monitoring system
Cologne
Future plans
Landlord dashboard to monitor the conditions in the properties.
Landlord & tenant can agree on reasonable limits.
Notes: If the humidity rises above a value of 60%, the tenant gets a push-message with a ventilation recommendation.
The tenant's behaviour can therefore be preventively influenced such that he/she has a better indoor climate, saves
heating costs and significantly reduces the risk of mould formation.
Planned for the future:
The landlord receives a dashboard, which allows him/her to monitor an overview of the conditions in the properties. In
the run-up, reasonable limits can be agreed with the landlord.

## Slide 12: Low Energy Districts Cologne
Project area
Mülheim
Stegerwaldsiedlung
Energy supply for:
    16 apartment blocks
    ~ 33.500 m² living space
    > 700 residential units
    > 1.000 tenants
PV-modules on all roofs (~5.600 m², 875 kWp)
41 air-water heatpumps (429 kWth)
District heating for peak loads (1.743 kW)
16 battery storage units (210 kW, 655 kWh)

## Slide 13
A cloud based energy management system for districts
Forecast with self-learning algorithms
Optimization with flexible goals
Connection to the RheinEnergie Virtual Power Plant
Low Energy Districts - Siedlungsmanagement
Cologne
Schematic illustration

## Slide 14
Forecast is based on weather data and historic data from the plants.
The quality is improving due to self learning algorithms.
Forecast for:
  Electricity consumption
  PV production
  Heat consumption
Low Energy Districts - Siedlungsmanagement
Cologne

## Slide 15
  Optimization
  Based on the forecast the energy production and consumption can be optimized
  Working fully automated and continuously for the whole district
  Different goals can be set
    Minimize usage of district heating
    Minimize grid supply
    Minimize feed-in into grid
  The optimization creates schedules for the plants for each building
Low Energy Districts - Siedlungsmanagement
Cologne

## Slide 16
  Connection to RheinEnergie’s VPP
  Based on the optimization, possible flexibility can be calculated
Available flexibility sent to RheinEnergie’s VPP
Based on the trading, result schedules are sent to the Energy Managers in each building
Low Energy Districts - Siedlungsmanagement
Cologne
The schedules for all buildings are calculated every 15min for the next 36 hours

## Slide 17
Low Energy Districts - Siedlungsmanagement
Cologne
DRAFT
  Visualization illustrating the flow of energy
Notes: We have commissioned a visualization which illustrate the flow of energy The values displayed have nothing to do with our settlement. This is only a draft at the moment. we are still in coordination

## Slide 18
DRAFT
Low Energy Districts - Siedlungsmanagement
Cologne
  Detailed view of producers and consumers
Also available as analysis report
Notes: you can get a detailed view of the producers and consumers. Information such as energy mix are displayed as well as performance and condition. Its also possible to get these information in an analysis report.
The values displayed have nothing to do with our settlement. This is only a draft at the moment. we are still in coordination

## Slide 19
RheinEnergie AG
Parkgürtel 24
D-50823 Köln
Corporate Development
c.remacly@rheinenergie.com
Christian Remacly

## Slide 20
Julia Egenolf
Tel +49 - 221 - 221- 29571 E-Mail julia.egenolf@stadt-koeln.de